## Slide 1: Directed Relation Graph with Expert Knowledge for Skeletal Mechanism Reduction
Tianfeng Lu, Zhaoyu Luo and Max Plomer
University of Connecticut
S.M. Sarathy and W.J. Pitz
Lawrence Livermore National Laboratory
Sibendu Som and Douglas E. Longman
Argonne National Laboratory
7th US Combustion Meeting Georgia Institute of Technology
Atlanta, GA
March 20, 2011
Thank you for the introduction
Good afternoon everyone
My topic for today discussion is “title”
The following people contributed to this project:
“list off names”

## Slide 2
Background
The Direct Relation Graph with Expert Knowledge (DRG-X) method for chemical reduction
Demonstration of DRG-X with large kinetic mechanisms
Summary
Outline
So for today’s discussion we will first talk about
“first bullet”
Then go into the “2nd bullet” methodology which we call DRGX
This we will show “3rd bullet”
And then we will summarize the important features that DRGX brings to chemical mechanism reduction

## Slide 3
Size of Fuel Mechanism (Lu & Law, 2008)
Background – Chemical Mechanisms
3329 species;10,806 reactions
As we see advancements in chemical kinetics, in recent years we have been able to develop much more detailed mechanisms for complex fuels such as biodiesl and md, methyldecanoate.
Blue corresponds to before the year 2000
Green coresponds to between the years 2000 and 2005
Red represents new mechanism after 2005
As you can see, before the year 2000, chemicals mechanisms were for the most part quite small, and for fuels of low carbon number such as methane, CH4
The size of the mechanism is proportional to carbon number. Having a large carbon number increases the possibly to break the molecule them in different places, resulting in different chemical pathways.
Adding additional complexity and size to a fuel mechanism.
[remember volume]
This picture is the # of species vs reactions for the typically available chemical mechanisms
You can see the biodiesel, LLNL is an extremely large mechanism, consisting of several thousand species and over 10,000 reactions. and in the future with progress in chemical kinetics we are expecting even larger mechanisms.
[carb #?]
Transition: Therefore mechanism reduction is an absolute necessity.
Necessity of Mechanism Reduction
  Detailed mechanism too large for CFD simulations
  Computational time ~ N2 ~ N3

## Slide 4
Methods of Skeletal Mechanism Reduction,e.g.
  Sensitivity analysis: Hwang et al,1983;Rabitz et al, 1989; Turanyi et al, 1990…
  Detailed reduction: Wang & Frenklach,1991
  Directed relation graph(DRG): Lu & Law,2005
  DRG-aided sensitivity analysis (DRGASA): Zheng et al, 2007; Sankaran et al, 2007
  DRG with error propagation (DRGEP): Desjardins-Pepiot & Pitsch,2008
  Path flux analysis (PFA): Sun et al,2010
Directed Relation Graph (DRG)
  Highly efficient: Reduction time linearly proportional to number of reactions
  Controlled reduction error
  Fully automated
Background – Mechanism Reduction
Detailed mechanism are quite important as they help us understand how these fuels function, especially with pathway analysis.
Although, due to their massive size, and limitations in computing power, detailed mechanisms must be reduced in size to be used in CFD simulations, because computational time is proportional to number of reactions squared.
Depending on the CFD application for instance, heat release might be the only importance parameter, and only the species than ensure accurate heat release are retained in the skeletal mechanism.
There are many methods of mechanism reduction, overall DRG based reduction methods have proven to be the most efficient, since the time it takes to reduce a mechanism using DRG is linearly proportional the number of reactions
It’s a necessity b.c. sometimes in CFD only heat release is of importance, so in that case you’d only want the species that are important for heat release in your skeletal mechanism. So in that instance, all other species are unimportant. Also since the computational time is proportional to the # of reactions ^2 or cubed.
There are many methods of reduction, as shown here.
So DRG is highly efficient due to the reduction time being linearly proportional to the number of reactions, it also allows the user to control reduction error.
Also DRG is fully automated
Transition: so how exactly does DRG work?

## Slide 5
If reaction i involves species B
otherwise
Direct species relation: species A directly depends on B if eliminating B induces immediate significant error to A:
AB
  If A is kept in skeletal mechanism and rAB>
  Then B should also be kept,
Indirect Species relation
  AB, BC  A C
Review of DRG Method (Lu,Law 2005)
A
B
D
C
The DRG method is based on the idea that during a combustion process, some species exist that are weakly coupled and do not significantly affect the reaction rates of the major species and can therefore be eliminated from the mechanism.
The error rAB, induced to a species A by the elimination of another species B for a given reaction states that consists of temperature and the species concentrations.
This whole term is the production rate of species A in reaction I
Delta_B_i is 1 if the reaction I involves species B
(Figure)
Take a look at our figure on the right showing the typical configuration of a directed relation graph.
BC and EF demonstrate strongly coupled species groups.
Even though A is not directly affected by C, removing C would greatly affect B, indirectly causing error in A.
If A is a major species, A, B, C would be kept for the skeletal mechanism
DRG is based on the idea that in a combustion process some species exist that are weakly coupled and therefore don't cause much error in our major species.
So we have our direct species relation: “read bullet”
rab which signifies the amount of error caused in the production rate of A if we remove B
-here is the production rate of A in reaction i, [the product of the reaction rate of reaction i and stoichiometric coefficent of A in reaction i]
If B is in reaction i then delta b i equalls 1, and if not then delta b i equals 0
AB meangs that A directly requires B
“read the middle bullets”
***Indirect species relation, means that A directly requires B, and B directly requires C, therfore A indirectly requires C.
***So here is our figure of a typical direct relation graph where A is a major species, such as an oxider, fuel or h radical , and will be our starting species. if you want to predict this guy correctly, you need to predict whatever it requires, A requires B, B should be retained, B requires C, C should be retained.
Transition: this DRG method offers certain advantages

## Slide 6
Advantages/Limitations of DRG
Advantages
  High efficiency (linear time reduction)
  Error control fully automatic
Limitation
  Lack of flexibility in controlling errors for different species/relations
Proposed solution:
DRG with expert knowledge (DRG-X)
DRG offers many important advantages, such as :
-efficiency, which makes it particularly suitable for reduction of extremely large mechanisms
-DRG is fully automatic, meaning that other important species are automatically retained by the graph searching algorithm.
-The DRG method requires as input one or a few major species as the search-initiating species, as well as a user-specified error tolerance.
-While having a uniform error tolerance renders DRG especially simple to apply, it nonetheless results in a lack of flexibility in tailoring the skeletal mechanism based on the uneven uncertainties in various reaction pathways in a large detailed mechanism.
For example if a skeletal mechanism only needs to be accurate for heat release and a few important species, a small reduction error must be specified and the reduction will be quite limited.
DRG-X solves this limitation, by allowing the user to specify important reaction pathways, in order to obtain a more accurate skeletal mechanism
Such as “high efficiency”, since the reduction time is linearly proportional to mechanism size
Error control fully automatic, DRG will automatically retain species that exceed the default error tolerance
The limitations of DRG some reaction rates are very accurate, some have larger error, doesn't make sense to accuracy predict the reactions with larger uncertainty, therefore if you want to use a species specific error tolerance, we can probably substantially further reduce the skeletal mechanism from DRG method, without sacrificing the chemical fidelity .
transition: SO if we specify important reaction pathways using this expert knowledge we can obtain a more accurate skeletal mechanism which is the heart of the DRGX method

## Slide 7
Basic Concepts of DRG-X
DRG-X is an enhanced DRG that allows species-specific error control (expert knowledge)
Expert knowledge (x-values)
  Assigned to selected species or heat release
    Indicate desired accuracy of species concentration/heat release rate
    Value between 0 and 1
    To achieve balanced chemical fidelity
To solve the limitations of DRG, in DRG-X reduction errors for important species are specified based on expert knowledge.
Species specific x-values, the expert knowledge, are specified for selected species.
The species associated with reactions with small uncertainties can be assigned a small x-value (0.1), large uncertainties…a large x-value. (0.3)
All other species are assigned a default error tolerance such as 0.5
If a pollutant is of interest for example, and needed to be predicted as higher accuracies than all other species, a small x-value (0.1) would assigned.
These x-values can then be pre or post processed, meaning that when pre processing the xvalues are used to expand the starting species set in the previous DRG.
IN Post processing, a normal DRG reduction is performed, then afterwards the species that are important to a species A based on its xvalues X_A are added back into the mechanism.
Some example species and parameters that xvalues can be assigned to are: pollutants, hradical, fuels, oxidizer, heat release
Because the errors in the skeletal mechanism roughly match the level of uncertainties in the detailed mechanism, overall chemical fidelity can be retained.
So….. “first bullet”
These xvalues different from epsilon,
Xvalue are SSET’s, while epsilon is a uniform error tolerance for species we don’t assign xvalues to.
“after 1st sub bullet”
For instance if you want a polutant such as nox or co2 to be quite accurate you can specify a small value for the xvalue of the pollutant.
“Last bullet”
by specifying these x-values we can retain the original/balanced chemical fidelity, but with a relatively larger reduction error threshold
Transition:
Now lets go into an example to show the differences between DRG and DRGX

## Slide 8
DRG vs. DRG-X, an Example
A
B
D
C
F
E
A
B
D
C
F
E
0.2
0.8
0.8
0.6
0.1
0.1
0.2
0.8
0.8
0.6
0.1
0.1
Default Error Tolerance:  = 0.3
Starting Species: A
DRG
DRG-X
xE = 0.1
you can specify an x-value for important species to retain the species and reaction pathways of interest
Left DRG
Right DRGX
red indicates non-trivial species dependences, black indicates trivial species dependencies
We are using a default error….of..
A is the starting species, from A you can reach B and C in DRG, therefore D E and F will be eliminated in DRG
what if we are interesting in retaining species E and the associated reaction pathways? in that case we can specify an X value for E, for example make Xe=0.1
by specifing 0.1 e will be retained in the skeletal mechanism, also the species strongly coupled with E will be retained, as a result the DRGX derived mechanism will have A B C E & F, but D will still be unimportant
Transition:
There is actually 2 options for integrating the x values in DRGX processing (1) pre processing and (2) post processing

## Slide 9
X-Values: Pre vs. Post-processing
Post-processing:
  Performs regular DRG reduction
  Adds species that cause error in important species greater than x-value back into mechanism
In our current study DRGX with postprocessing, which adds important species based on their x-values after a normal DRG reduction, was found to be a good option when deriving skeletal mechanism if the user wants to balance mechanism size and chemical fidelity
pre proessing good for chemical fidelity
Pre-processing builds a large starting species set of:
  Important species with x-values
  Any species that cause error in important species greater than x-value
A
B
0.2
0.1
0.8
A
B
0.2
0.1
0.8
Default Error Tolerance:  = 0.4
Starting Species: H
C
0.5
C
0.5
xA = 0.2
xA = 0.2
we want to demonstrate the difference between preprossing for the same epsilon and for the same xvalue
again red means strong coupling, black means weak coupling
“Preprocess bullets”
“postprocess bullets”
we specified an x-value for A, X_a = 0.2 , therefore any edge from A larger than 0.2 would be retained
For preprocessing we would include A and everybody A can reach, A and B would be included in the starting species set, searching with DRG with epsilon =0.4 B->C this edge would also be important
Therefore A B and C would be included in the skeletal mechanism
but for the post processing case, we do regular DRG search with epsilon=0.4, from the DRG search A B C would be eliminated
but if you specify x value for for species A, 0.2, A would be put back into mechanism, and because A requires B strongly, B will be retained, but it doesn't go any deeper so you wont have C, C is not directly required by A
so the pre and post, pre may have larger mechanism, because post processing only retain the psecies of special interest and the species directly required
pre processing it will retain the species of special interest and all the species either directly or indirectly required
H
H

## Slide 10
Demonstration of DRG-X (I)
n-Dodecane (LLNL, C8-C16 alkanes)
2115 Species, 8157 Reactions
(Westbrook et al, 2009)
The first application of DRGX was performed on the n-dodecane mechanism, which is used as a surrogate for jet fuel.
The DRGX method was first investigates using this mechanism.
The detailed mechanism was provided by Lawrence Livermore nation laboratory, and featured 2115 species and 8157 reactions.

## Slide 11
Reduction Curve of DRG and DRG-X
For small threshold ,
DRG-X reduces to DRG
Most of reduction can be performed using small error tolerances
 >0.7 DRG-X curve plateaus
  species needed for heat release
DRGX differs from DRG for  0.4
Here we have a comparison of the reduction curves for DRG and DRGX with both pre and post processing.
This is an autoignition of a stoichiometric mixture of n-dodecane and air at a pressure of 10 atm and initial temperature of 850K
An x-value for heat release of 0.1 is used in DRGX
The solid red line is DRG
The uniform dotted like is DRG preprocessing
And the varying length dotted line is DRG with post processing
You can see for small threshold errors such as epsilon<0.2, the reduction curves are identical.
Also for small thresholds you notice a very steep section, indicating that much of the reduction can be achieves with small error tolerances.
For larger thresholds, such as epsilon>0.4 DRGX with preprocessing features the largest mechanism, DRG yields smallest.
When epsilon>0.7 we notice that the DRGX curve plateus, this is because a set of species are retained due to the small x-value for heat release, then very few additional species can be eliminated by increasing the threshold value
When comparing DRG pre and post processing: you notice that around a threshold value of 0.6 , DRGpre has slightly more species, these species were picked up when the graph searching algorithm found species that caused error in the expanded starting species list of the DRGpre
SO here is the reduction curve comparing DRG and DRGX
Mention X axis y axis
a stoichiometric mixture of n-dodecane and air , with P=10atm and T0=850K
solid line is the detailed mechanism
xvalue of 0.1 was used for heat release in DRGX
previous DRG we didn't consider the heat release effect, but here in DRGX we can specify different error tolerances for heat release
we can justify this because in many applications people are more interested in accurate prediction of heat release
“goes through bullets”
“last bullet”
For E=0.4 DRGxpre becomes the largest mechanism and DRG becomes the smallest

## Slide 12
Accuracy in Autoignition
DRGX/pre features most accurate post-ignition temperature
Speech:Very small e value, DRGX reduces to DRG
Here we have the temperature profiles of a few different skeletal mechanisms developed using the 3 approaches, varying threshold error.
Once again this is an autoignition of a stoichiometric mixture of n-dodecane and air at a pressure of 10 atm and initial temperature of 850K
When specifying a small threshold error epsilon=0.2, the 3 methods result in the same skeletal mechanism, and DRGX reduces to DRG. The circles. The 449 species mechanism generated is quite accurate, but still large.
The next 3 mechanism using DRG and DRG pre and post processing used an aggressive value of epsilon 0.5
The 3 mechanism had sizes of 160 for DRG, 184 for DRGX post processing and 208 for DRGX preprocessing.
The errors for these mechanism are just as predicted with DRG featuring quite large errors.
This is quite impressive, the 208 species mechanism from DRGX preprocessing is nearly the same error as the low threshold DRG mechanism over twice its size.
This thereby demonstrates the power of DRGX
(2115 species)
(449)
(160)
(184)
(208)
Expert info:
XQ=0.1
so here we are comparing our 3 methods DRG and DRGX with pre and post processing
ndodecane and air stoichiometric mixture p=10atm T0=850K
Xvalue of ___used for DRGX
THis graph represents temperature vs resonance time in an autoignition simulation
line is detailed mechanism
Note that for small error tolerances DRGX reduces to DRG, which is the same mechanism
which is quite accurate but very large
“last bullet”
and the DRG with the similar uniform error tolerance had the worst error.
Transition: so now we see the effec that different epsilons have , but what if we vary the xvalue for heat release?

## Slide 13
Accuracy in Autoignition (cont.)
Decrease in xQ features even greater temperature accuracy
Contining from last slides, Once again we have an autoignition of a stoichiometric mixture of n-dodecane and air at a pressure of 10 atm and initial temperature of 850K
This figure shows the effect of a fixed threshold of epsilon =0.5 and changing the x-value for heat release from 0.1 to 0.01
The solid line is the detailed mechanism
Dotted line is the DRGX with xvalue of 1/10 for heat release
Circles are DRGX with xvalue of 1/100 for heat release
This nearly doubles the size of the mechanism from 208 species to 368 species, but the accuracy in temperature is improved greatly.
From this figure and the previous slides, You now should have a feel for the effect of different x-values and epsilon values have on the size and accuracy of the resulting skeletal mechanisms for DRG and DRGX.
(2115 species)
(208)
(368)
Well “first bullet”
with same parameters as previous autoignition of a stoichiometric mixture of n-dodecane and air
As we decreased the x-value for heat release we saw much greater temperature accuracy, but also double the size of the mechanism.

## Slide 14
DrgX was futher investigates using a tri-component biodiesel surrogate mechanism
The detailed mechanism was provided by Lawrence Livermore national laboratory, and featured 3299 species and 10806 reactions.
The molar concentration of the mixture is
¼ methyl decenoate
¼ methyl 9 decenoate
½ n-heptane
Argonne uses the mechanism
Demonstration of DRG-X (II)
A Tricomponent Biodiesel Surrogate:
25% Methyl Decenoate,
25% Methyl-9-Decenoate (MD9D),
50% n-Heptane
(LLNL Mechanism,
3299 Species, 10806 Reactions
Herbinet et al, 2010)

## Slide 15: X-Values for Species
Here is our 56 species-specific x-values ranging from 0.1 to 0.3 for set 2 of the previous slide.
The chemical fidelity of the reactions that feature these species will be preserved to the desired amount.
This enables the user to conduct detailed pathway analysis on a reduced mechanism.
(Specified by S.M. Sarathy and W.J. Pitz)

## Slide 16
Reduction Curve of DRG-X Preprocessing
Set 1 (540 species):
xQ=0.1,
xh=0.3
Set 2 (1504 species):
xQ=0.1,
56 species-specific x-values
Here we have a comparison of the DRGX preprocessing reduction curves of two sets of expert knowledge for the biodiesel mechanism.
This reduction used both autoignition and perfectly stirred reactor, PSR
The parameter range was
equivalence ratio from 0.5 to 2.0
pressure from 1 to 100 atm
Initial temperature from 700 to 1800K for auto-ignition.
Initial temperature of 300K for Perfectly stirred reaction
Set 1 is a solid black line and set2 is a dotted blue line.
Set 1 features only xvalues for 0.1 for heat release and 0.3 for production of h-radical
Set 2, in addition for an xvalue of 0.1 for heat release features an expanded list of x-values for species of important reaction pathways.
While the x-values in Set 1 can be used to obtain smaller mechanisms that is good to predict the overall system parameters such as ignition delays and extinction time, the x-values in Set 2 can be used to obtain skeletal mechanisms with high chemical fidelity, for detailed reaction pathway analysis.
You notice that the reduction curve of Set 1 is much steeper than that of Set 2, and that is due to the additional high accuracy requirements, which allows higher chemical fidelity for the species list in the following table.
1504 species
540 species
.
.
So here is the reduction curve of DRGX for our biodiesel tri-surrogate mixture, and we have the # of species vs the threshold value
We had to different sets of xvalues, which then created two different mechanisms
“describe sets”
Set 1 is our solid line, set 2 is our dotted line
Set1 has a much steeper curve because of the high accuracy reqs for set 2
transition for next slide: we selected an error tolerances of 0.5 resulting in two different mechanisms, “sizes” next lets look at how the mechanisms validate

## Slide 17
Mechanism Validation: Autoignition
Here we have a comparison of the detailed biodiesel mechanism, with both set 1 and 2, which we just previously discussed, both using DRGX preprocessing with two sets of expert knonwledge.
The parameter range was
equivalence ratio from 0.5 to 2.0
pressure from 1 to 100 atm
Initial temperature from 700 to 1800K for auto-ignition.
Initial temperature of 300K for Perfectly stirred reaction
Autoignition is on the left which features ignition delay as a function of the inverse of temperature.
And perfectly stirred reactor, PSR, is on the right, which features temperature as a function of resonance time. PSR has a stable upper branch, and unstable middle branch. The turning point is conventionally defined as the extinction point.
-The line is the detailed 3299 species mechanism from LLNL.
-The circle is the 1504 species DRGX mechanism of Set2 with an extended list of high accuracy requirements just shown in the previous table.
-The plus is the 540 species mechanism, with only xvalues for heat release and h radical production
Both mechanisms agree well with the detailed mechanism, mainly because these plots only reflect heat release, the chemical fidelity preserved in the mechanism of extended x-values will be shown in the next slide.
Similar accuracy for mechanisms from Set I vs Set II
This is the validation the global parameter of ignition delay which strongly depends on heat release, these two mechanism have similar accuracy for ignition delay (possibly inaccurate for other things though)
Lean case left, rich right
This agreement is not suprising that both match well because of the small xvalue of 0.1 specified for heat release. Therefore if you want to look at heat release, the global parameters should agree well with the detailed mechanism.
Transition:
And the mechanisms validate equally well for extinction point, another heat release dependent global parameter

## Slide 18
Mechanism Validation: Perfectly
Stirred Reactor
Here we have a comparison of the detailed biodiesel mechanism, with both set 1 and 2, which we just previously discussed, both using DRGX preprocessing with two sets of expert knonwledge.
The parameter range was
equivalence ratio from 0.5 to 2.0
pressure from 1 to 100 atm
Initial temperature from 700 to 1800K for auto-ignition.
Initial temperature of 300K for Perfectly stirred reaction
Autoignition is on the left which features ignition delay as a function of the inverse of temperature.
And perfectly stirred reactor, PSR, is on the right, which features temperature as a function of resonance time. PSR has a stable upper branch, and unstable middle branch. The turning point is conventionally defined as the extinction point.
-The line is the detailed 3299 species mechanism from LLNL.
-The circle is the 1504 species DRGX mechanism of Set2 with an extended list of high accuracy requirements just shown in the previous table.
-The plus is the 540 species mechanism, with only xvalues for heat release and h radical production
Both mechanisms agree well with the detailed mechanism, mainly because these plots only reflect heat release, the chemical fidelity preserved in the mechanism of extended x-values will be shown in the next slide.
Similar accuracy for mechanisms from Set I vs Set II
“Say pressures”
Again because of such a small xvalue, the extinction times are quite accurate for our two mechanisms
Transition:
However lets next see if its the same conditions for species profiles.

## Slide 19
Further Validation: Autoignition
Species Concentration
Here continue our comparison of the detailed biodiesel mechanism, with set 1 and 2, both using DRGX preprocessing with two sets of expert knowledge.
To futher show the difference of chemical fidelity between the two skeletal mechanisms, we Compare the species concentrations calculated using the detailed and skeletal mechanisms for auto-ignition of stoichiometric biodiesel-air at pressure of 10atm and initial temperature of 850K.
-The line is the detailed 3299 species mechanism from LLNL.
-The circle is the 1504 species DRGX mechanism of Set2 with an extended list of high accuracy requirements just shown in the previous table.
-The plus is the 540 species mechanism, with only xvalues for heat release and h radical production
On the left we see the concentration of selected major species including MD, CO, H20, which are important for heat release.
No surprise here, that all skeletal mechanisms agree closely since the same x-value for heat release was used for both mechanisms.
The diffrences come when we examine the intermediate species on the right.
Our mechanism which features additional x-values for these intermediate species, is much more accurate.
Both of these mechanism can be quite useful,
The smaller sk540 can be useful in practical engine simulations after futher reduction, and our larger sk1504 would be great
Similar accuracy for major species
C2H2 CH3 H
Set I default .. 0.3
Set II 0.2 0.1 0.1
left panel tells us the concentation for major species , while the right hand side is the intermediate species for which we specified different xvalues
We had similar accuracy for the major species, but not the minor species
‘mention the two sets of xvalues/error tolerances’
-for set 1 we had the default error tolerance of .5 for c2h2 and ch3, and an xvalue of 0.3 for H radical
-for set two we had lower tolerances for each because of assigning xvalues
We used these 3 species md co and water to show what happened to the major species
MD when higher concentration all agree very well, this is because we specified the same heat release xvalue
WHen the fuel becomes very low in concentration its not that important for heat release any more
For the intermediate species on the right we can see a major difference , which shows the effect of the different xvalues on the species in teh skeletal mechanism

## Slide 20
Summary
DRG-X formulated for species-specific error control
N-Dodecane & biodiesel mechanism used for demonstration
Usage of DRG-X
1. Mechanism reduction for detailed kinetics study
2. May result in smaller mechanisms by allowing larger , and small XQ
I would like you to leave to today with two points about DRGX

## Slide 21: Acknowledgements
The work at University of Connecticut was supported by the National Science Foundation under Grant 0904771.
The portion of this work supported by LLNL was performed under the auspices of the U.S. Department of Energy by Lawrence Livermore National Laboratory under Contract DE-AC52-07NA27344.
The submitted manuscript has been created by UChicago Argonne, LLC, operator of Argonne National Laboratory (Argonne). Argonne, a U.S. Department of Energy Office of Science laboratory, is operated under Contract No. DE-AC02-06CH11357.

## Slide 22: Thank You